## Slide 1
IP Telephony
2020

## Slide 2
IP Telephony Applications
Integration of data, voice and fax
  single network saves cost
Multiple sound quality levels
  higher or lower than telephone
Video telephony
Unified Messaging
Web-based calling (click-to-call)
Low-cost voice calls

## Slide 3
IP Telephony Applications (cont.)
Real-time billing
Remote teleworking
Enhanced Teleconferencing

## Slide 4
Components of a VoIP Network
IP Network
  Carries both media (voice) and signalling
End-points
  Encoder
  Packetiser
Call control
  Independent of Call routing
Gateways
  to PSTN and other networks

## Slide 5
Call Control
Controlling the setting up and features of calls
Additional features such as call transfer, call forwarding and conferencing
Billing
Security and Authentication
Call control is distinct from voice transmisssion
Several VoIP call control standards

## Slide 6
Session Initiation Protocol (SIP)
IETF Standard
Light-weight compared with H.323
Text-based client-server protocol
Features such as:
  Call forwarding
  Callee and calling number identification
  Personal mobility
  Caller and callee authentication
  Basic Automatic Call Distribution (ACD)

## Slide 7
SIP (cont.)
SIP creates, modifies and terminates sessions with one or more participants.
Session Types:
  Internet multimedia conferences
  Internet telephone calls
  Multimedia distribution

## Slide 8
Main functions
Signaling
  Carry call information across network
Session Management
  Control attributes of end-to-end call

## Slide 9
SIP Architecture
Peer – to – Peer Protocol
Peers in a session are called User Agents (UA)
Functions of a UA
  User Agent Client (UAC)
    Client application that initiates SIP request
  User Agent Server (UAS)
    Server application which respond to SIP request
Physical Components
  SIP Clients
  SIP Server

## Slide 10
SIP Clients
Phones
  Can act as either UAC or UAS
  Can initiate SIP request and respond
  IP phones, Soft phones
Gateways
  Provide call control
  Translate between SIP end points
  To PSTN for telephony interworking
  To H.323 for IP Telephony interworking

## Slide 11
SIP Servers
Proxy Server
  Forward received SIP request
  Authentication, Authorization, Routing, security
  Network Access Control, Reliable retransmission
Redirect Server
  Provide info. about next hop (s)
Registrar server
  Register locations of UAC
  Co-located with proxy & redirect Servers

## Slide 12
SIP Architecture …

## Slide 13
How it works
Users identified by unique SIP address
  sip:userid@gateway.com
  UserID – username or E.164 address
    sip:alan@wcom.com
    sip:+1-613-555-1212@wcom.com;user=phone
Users register with registrar server
When initiating a call
  SIP request Header
    From : Caller Address
    To : Callee Address

## Slide 14
SIP Methods
INVITE Requests a session
ACK Final response to the INVITE
OPTIONS Ask for server capabilities
CANCEL Cancels a pending request
BYE Terminates a session
REGISTER Sends user’s address to server

## Slide 15
SIP Responses
1XX Provisional 100 Trying
2XX Successful 200 OK
3XX Redirection 302 Moved Temporarily
4XX Client Error 404 Not Found
5XX Server Error 504 Server Time-out
6XX Global Failure 603 Decline

## Slide 16
How it works …
SIP Session
200 OK
ACK
INVITE sip:user@sip2.com
host.sip1.com
sip.sip2.com
SIP
User Agent
Client
SIP
User Agent
Server
BYE
200 OK
Media Stream

## Slide 17
SIP INVITE
INVITE sip:e9-airport.mit.edu SIP/2.0
From: "Dennis Baron"<sip:6172531000@mit.edu>;tag=1c41
To: sip:e9-airport.mit.edu
Call-Id: call-1096504121-2@18.10.0.79
Cseq: 1 INVITE
Contact: "Dennis Baron"<sip:6172531000@18.10.0.79>
Content-Type: application/sdp
Content-Length: 304
Accept-Language: en
Allow: INVITE, ACK, CANCEL, BYE, REFER, OPTIONS, NOTIFY, REGISTER, SUBSCRIBE
Supported: sip-cc, sip-cc-01, timer, replaces
User-Agent: Pingtel/2.1.11 (WinNT)
Date: Thu, 30 Sep 2004 00:28:42 GMT
Via: SIP/2.0/UDP 18.10.0.79

## Slide 18
Session Description Protocol
IETF RFC 2327
“SDP is intended for describing multimedia sessions for the purposes of session announcement, session invitation, and other forms of multimedia session initiation.”
SDP includes:
  The type of media (video, audio, etc.)
  The transport protocol (RTP/UDP/IP, H.320, etc.)
  The format of the media (H.261 video, MPEG video, etc.)
  Information to receive those media (addresses, ports, formats and so on)

## Slide 19
SDP
v=0
o=Pingtel 5 5 IN IP4 18.10.0.79
s=phone-call
c=IN IP4 18.10.0.79
t=0 0
m=audio 8766 RTP/AVP 96 97 0 8 18 98
a=rtpmap:96 eg711u/8000/1
a=rtpmap:97 eg711a/8000/1
a=rtpmap:0 pcmu/8000/1
a=rtpmap:8 pcma/8000/1
a=rtpmap:18 g729/8000/1
a=fmtp:18 annexb=no
a=rtpmap:98 telephone-event/8000/1

## Slide 20
Name translation and user location
Caller only has callee's name or e-mail address.
Need to get IP address of callee’s current host:
  user moves around
  DHCP protocol
  user has different IP devices (PC, PDA, car device)
Result can be based on:
  time of day (work, home)
  caller (don’t want boss to call you at home)
  status of callee (calls sent to voicemail when callee is already talking to someone)
Service provided by SIP servers:
  SIP registrar server
  SIP proxy server

## Slide 21
SIP Registrar
REGISTER sip:domain.com SIP/2.0
Via: SIP/2.0/UDP 193.64.210.89
From: sip:bob@domain.com
To: sip:bob@domain.com
Expires: 3600
When Bob starts SIP client, client sends SIP REGISTER message to Bob’s registrar server
(similar function needed by Instant Messaging)
Register Message:

## Slide 22
SIP Proxy
Alice send’s invite message to her proxy server
  contains address sip:bob@domain.com
Proxy responsible for routing SIP messages to callee
  possibly through multiple proxies.
Callee sends response back through the same set of proxies.
Proxy returns SIP response message to Alice
  contains Bob’s IP address
Note: proxy is analogous to local DNS server

## Slide 23
How it works …

## Slide 24
How it works …

## Slide 25
How it works …

## Slide 26
Instant messaging based on SIP
SIMPLE – IM protocol based on SIP
SIP promises interoperability between various IM vendors
“Forking proxy “
SIP has unique user tracking features.
SIP addressing

## Slide 27
Instant Messaging (Contd.)
SIP Client
SIP Client
dynamic.com
columbia.edu
SIP Redirect server
SIP proxy
foo.com
Location
service
proxy
sales.foo.com
1
2
3
4
5
6
7
8
9
10
11
12
13

## Slide 28
Features of SIP
Simple
  Similar to SMTP & HTTP
  Use MIME to carry extra information
Scalable
  Distributed functionality support scalability
Interoperable
  Open standard
Mobility
  Support using proxying & redirecting
  Use of IP phones, PC, regular phones